## Slide 1: Introduction to Hardware Attacks
Josh Rabinowitz

## Slide 2: Agenda
Day 1– Introduction
Day 2– Board & Components
Day 3– External Interfaces I
Day 4– External Interfaces II
Day 5– Conclusion

## Slide 3: Day 1

## Slide 4: Introduction

## Slide 5: Why Hardware Security?
Consider your attack surface…

## Slide 6: Why Hardware Security?
Consider your attack surface…

## Slide 7: Why Hardware Security?
Consider your impact…

## Slide 8: Why Hardware Security?
Consider attack routes and effort…

## Slide 9: Why Hardware Security?
Consider attack routes and effort…

## Slide 10: Why Hardware Security?
Consider attack routes and effort…

## Slide 11: Example
(ACTUAL) Hardware driver bug – can you spot the problem?

## Slide 12: Example

## Slide 13: Secure Hardware Design
Upper layers protected by lower layers
Layers of trust
  Code signing
  Exploit mitigations
  Cert pinning, encryption
  Write protections
  Access controls
  MFA
Root of trust/Anchor
  Baked into silicon
  Unique to device
  Unknown to vendor
Strong key management

## Slide 14: ACTUAL Hardware Design…
Chains of trust rarely extend below OS
Absent code signing
Vulnerable supply chains
Wide open debug access
Leaked/unprotected MFG tools
Direct access to filesystems

## Slide 15: ACTUAL Hardware Design…
HW security ~15yrs behind SW security
Fewer attackers, mostly due to equipment costs
MOST consumer electronics are “fish in a barrel” to the skilled attacker
This is improving as tools grow cheaper and more accessible at hobbyist level…

## Slide 16: Embedded Systems
Definition: “An embedded system is a system that has a software embedded into computer-hardware which makes a system dedicated for an applications or specific part of an application, product or part of a larger system.”
Device includes programable CPU, not intended as general-purpose computer
(Essentially: Computers that don’t LOOK like computers!!)

## Slide 17: Embedded Device Architecture

## Slide 18: Finding Bugs
Reading specs
  Design bugs found by careful read
Reading errata
  Implementation bugs, reported w/workarounds
  Often have undocumented security impact
Fuzzing external interfaces
  Anything w/protocol  potential SW bugs
Glitching & Fault Injection
  Manipulating power/clocks
  Localized failures induced w/lasers
Invasive circuit/silicon modification
  Bypass protection circuits
  Internal data bus taps

## Slide 19: Finding Secrets
What are we after?
User Data
  Passwords, emails, documents, photos, contacts, etc.
Software
  1st step to RE is obtaining a copy
Intellectual Property
  Counterfeiting
  Industrial espionage
  Competitive Analysis
Network Access
  Pivot from device to other nodes
  Gaining persistence
Surveillance
  Control sensors (camera, mic, GPS, accelerometer, etc.)

## Slide 20: Finding Secrets
What do we look?
Common storage
  Volatile
    DRAM/DDR/LPDDR
    SRAM
    Registers
  Persistent (on-chip, off-chip, removable)
    Flash
    EEPROM
    EPROM
    OTP/Fuses
    ROM
  Cloud (not HW but may obtain credentials!)

## Slide 21: Common Findings
Memory
  Unencrypted memories
  Accessible signals
Secure Boot
  Incomplete chain-of-trust
  TOCTOU
  Partial signing
  Fail open
Defenses reliant on untrusted data
  Boot mode pins
  Flags in flash memory
Debug access
  JTAG, UART, test points
Privileged modes
Privacy controls
Equivalence of sensors 

## Slide 22: Time-bound Assessments
Areas of focus:
Secure-boot chain
  Boot-time firmware validation
Firmware update
  Bypass secure boot?
Storage
  Extract sensitive assets
  Inject malicious code/data
Attackable interfaces
  Start w/most external/privileged
  network, USB, debug
  New/proprietary/complex drivers
Things to skip:
Well-researched components
Hard to reach/unprivileged code
Unrealistic threats
Vendor code (Linux, AOSP, libs)
  DO check known issues!
    Outdated code/libs
    CVE’s
    Certain ‘insecure’ vendors (Mediatek, Synaptics, etc.)

## Slide 23: Case Study: Device Overview

## Slide 24: The Almond+ Router
Securifi Almond+
https://www.securifi.com/rg/almondplus
https://www.amazon.com/Securifi-Almond-Touchscreen-Wireless-Automation/dp/B00R0C2U5E

## Slide 25: Case Study: Setup

## Slide 26: “3-Minute Setup”
More like ~20 minutes…
Once setup/connected:
  Create user data
  Explore (attackable) functionality
  Do this before tearing open!

## Slide 27: Case Study: Teardown

## Slide 28
Quick step – expose the board WITHOUT doing damage
Be careful with antennas, display connector

## Slide 29
Keep this module handy, we’ll need it to power the main board!

## Slide 30: Day 2

## Slide 31: The PCB – At a Glance

## Slide 32: Basic Circuitry
Resistors
Capacitors
Diodes/Triodes
Inductors
Transistors
Oscillators
Buttons/Switches

## Slide 33: Recognizing Through-Hole vs Surface Mount
Components are fixed to a PCB using either plated “through-holes” (PTH/THT) or surface mount design (SMD/SMT)
Note that PTH and SMD components will look different
  Images on the left are all resistors, on the right capacitors
  Images on top are for SMD, bottom are for PTH
Useful resource for recognizing SMD components:
  https://www.pcbonline.com/blog/how-to-identify-smd-components.html
As we’ll see later, this concept applies to connectors and hardware interfaces in addition to components

## Slide 34: Through-hole vs. Surface Mount - Example

## Slide 35: Integrated Circuits
Analog
  Regulators
  Op-Amps
  A-D Converters
  RF IC’s
  Temp Sensors
Digital
  CPU’s, MCU’s, SoC’s
  Communication/Management IC’s
  Memory

## Slide 36: Integrated Circuits - Packages
Package types are classified in various ways:
  Through-hole vs SMD
  Shape – e.g. rectangular, square, linear
  Size/thickness
  Pin count
Note: not all package types/names are shown above…there are MANY more!

## Slide 37: Integrated Circuits - Packages
As an attacker, the package type alone provides some help:
  With experience, an attacker may deduce a chip’s function based on package type
  Package will determine what tools we can use to interface with the chip
    Chip-On vs. Chip-Off
    Chip-clip. Pin-clips, socket, etc.
  Some IC’s come in more than 1 package type, and share a datasheet– we’ll need to identify the appropriate version to obtain the right pinout

## Slide 38: Integrated Circuits – Packages
Example 1: BGA
As there are no ‘legs’ (pins) protruding visibly from the IC’s pictured here, we can deduce they use Ball Grid Arrays
They’ll need to be removed before we can interface or determine the pinout
Commercial socket/reader is the ideal tool, as “deadbugging” (soldering to individual pins) would require unreasonable effort

## Slide 39: Integrated Circuits – Packages
Example 2: TSOP-48
This IC is packaged as a Thin Small Outline Package with a total of 48 pins – a common package for NAND flash chips
Standard test clamps (“chip-clips”) are not widely available for this package…
Some Chip-On solutions:
  Xbox “360 Clip”
  https://360-clip.com/
  Delta Probe
  https://www.adapt-plus.com/products_html/8800-0150.html

## Slide 40: Common Ports & Interfaces

## Slide 41: The PCB Itself
In addition to the board’s components, we can study the board itself to learn more
Traces – can we determine how the board’s components are connected?
Via’s – may allow us to trace routes between layers
Ground layer– without a GND pin, we can use this layer as a reference when probing the board

## Slide 42: The PCB Itself – Silkscreen
Layer of ink which may contain:
  Safety/regulatory markings
  Component symbols
  Placement markers
  Pin indicators
  Logo’s, branding
May ease assembly/manufacturing, improve appearance, or provide user clarity

## Slide 43: The PCB Itself – Silkscreen
Silkscreen symbols for components, known as reference designators, are of particular interest to an attacker
There are 2 standards which outline reference designators for various components, including:
  IEEE 315-1975
  ASME Y14.44-2008

## Slide 44: The PCB Itself – Silkscreen
Knowing which markings and symbols are useless to the attacker will save precious time
For instance:
  https://www.ipc.org/system/files/technical_resource/E7%26S22_02.pdf
  Various standards exist for marking materials/finish
  Seen on both chips and PCB’s
  Untrained eye may confuse these for component symbols, chip numbers, etc.

## Slide 45: The PCB Itself – Test Points
Most manufactured PCB’s are littered with small copper pads. These are used during production to probe the board’s circuitry and monitor/inject test signals (using bed-of-nails or flying probe machines)
Most test points are useless to an attacker; however, as we’ll explore later, they sometimes provide hidden access to a critical interface (JTAG, UART, etc.)
Additionally, probing with a multimeter may tell us about the board’s Logic-Levels

## Slide 46: The PCB Itself – Ports/Headers
In addition to scattered test points, a PCB may contain ports, headers, and other standard breakouts for physical connection
Chips themselves utilize “external interfaces” for communication, debugging, flashing, etc.
Ports/headers provide easy outside access without removing chips or modifying circuitry
As an attacker, these are of significant interest as they may provide direct routes for attack
We’ll explore the most common external interfaces and how to approach them in later sections

## Slide 47: The PCB Itself – Other Concepts
Length Matching
  For high-speed applications, small timing mismatch can prevent proper wired communication (especially for synchronous protocols)
  To prevent mismatched signals, length-matching may be used when routing traces
  An attacker should spot the use of convoluted traces which may hint at an attack path

## Slide 48: The PCB Itself – Other Concepts
Trace Width
  PCB traces either carry signals or power; as power traces require more current, power traces are typically wider than signal traces
Pad Shapes
  A grounded (GND) pad can be spotted by the crosshair shape in the soldermask
  A squared pad juxtaposed by circular pads usually indicates a power (Vcc) pad

## Slide 49: Secure PCB Design
As we’ve seen, an experienced attacker may simply glance at the exposed PCB and glean information such as:
  Primary components
  Basic architecture and operation
  I/O Capabilities, Storage, Power
  External Interfaces
  Required attack tools
  Plausible attack paths
In many cases, a security-conscious designer can make simple modifications to discourage or slow down attackers at this starting phase

## Slide 50: Secure PCB Design
Heavy Layering; Blind/Buried Via’s
Buried Traces
No Silkscreen/symbols
Removed/disabled components
Missing pull-up/pull-down resistors
Severed traces
Shielded/covered circuitry
Unpopulated connectors
Sanded chip #’s

## Slide 51: Exercise – Spot the difference(s)
The following slide contains images of:
  An older SSD from Intel (left)
  A recent SSD from Intel (right)
Can you point out 2 design changes Intel has made over the years to make their drive more secure? (Hint: look closely…)

## Slide 52: Exercise – Spot the difference(s)

## Slide 53: Basic Probing
Important Skills:
Checking pin voltages
GND & continuity testing
Determining logic-levels
Multimeter is often the 1st tool a hardware hacker will reach for…know how to use it!

## Slide 54: Case Study: PCB

## Slide 55: Quick Glance Time…
With our target device opened and the board exposed, what can we identify…?

## Slide 57
Populated connectors
Unpopulated connectors
Unpopulated IC?
Removed/Option resistors?
  (pull-up, open-drain, etc.)
Pins (mostly) labeled 

## Slide 58: Chips & Datasheets

## Slide 59: Chips– Looking Closer
Chip Markings
  “Chip Number”
  Manufacturer Name/Logo
  Designators for lead content/plating finish
  QR Codes (often)
Polarity Markings
  Notch/Dot – Indicates Pin 1
  Pin numbers increase moving CCW around the chip

## Slide 60: Chip Numbers
Most chips have a 2-part serial number (i.e. “MC74HC00”)– typically the top marking
  Company Prefix (MC=Motorola)
  Chip type/specs (74HC00=Quad 2-input NAND)
Chips may have additional proprietary notations; for instance, small Micron chips have FBGA codes for lookup using their part decoder
Attackers will usually recognize manufacturer codes and logo’s (https://www.ultralibrarian.com/2020/09/15/list-of-ic-manufacturer-codes-ulc)

## Slide 61: Chip Numbers– More Examples
Note that every manufacturer uses slightly different format/nomenclature, but with the same basic structure

## Slide 62: Obtaining Datasheets
Resources
  Datasheet Archives (alldatasheet.com, datasheets.com, etc.)
    Full or Partial/Similar Number Search
    Narrow by package, function, etc.
  Electronics Distributors (Digi-Key, Mouser, Arrow, etc.)
    Datasheets often provided on product pages

## Slide 63: Datasheets – Brief Introduction
During initial teardown, the datasheet may help us to just identify the chip
When diving deeper, we’ll look for things such as:
  External Interfaces
  Pinouts
  Signal/Bus Descriptions
  Proprietary Command Sets
  Latching/Timing Diagrams
Later in the course we’ll extract this information from the datasheet of a NAND flash chip and use it to build an improvised chip-reader

## Slide 64: Case Study: Component Identification

## Slide 65
Chip Number | Vendor | Function | Details/Datasheet
(...) | (...) | (...) | (..)
Look closer at the target board and try to identify any chip numbers you can
Keep your findings organized using a table like the one above
This part may take a bit; be resourceful
  Google translate, new company names, etc.
  Some chips (especially obsolete ones) will be hard/impossible to find..

## Slide 66
(back side)

## Slide 67
The following can be found using a few quick searches:
Chip Number | Vendor | Function | Details/Datasheet
WPCS7542E A1 | Cortina (now Inphi Corp.) | Controller | "Advanced Network Processor with 2xCPU; 3xGE; 6xTS; Crypto; 3xPCIe; 4xSATA; LCD;2xPCM; 800Mhz, 625 PIN BGA" https://www.arrow.com/en/products/wpcs7542e.a1-900306/inphi-corporation
K4B2G1646Q-BCK0 | Samsung | (x2) SDRAM | https://www.datasheets.com/en/part-details/k4b2g1646q-bck0-samsung-electronics-55374854#datasheet
S34ML04G100TFI003 | Spansion (now Cypress) | SLC NAND Flash | https://pdf1.alldatasheet.com/datasheet-pdf/view/464250/SPANSION/S34ML04G100TFI003.html
EM357 | Silicon Labs | Zigbee SoC | https://www.silabs.com/documents/public/data-sheets/EM35x.pdf
ZW0301 |  | Z-wave controller | https://www.keil.com/dd/chip/4478.htm
QCA8337-AL3C | Qualcomm Atheros | Ethernet Switch | https://github.com/Deoptim/atheros/blob/master/QCA8337-datasheet.pdf
QCA9880-BR4A | Qualcomm Atheros | WLAN SoC | https://www.qualcomm.com/products/internet-of-things/networking/wi-fi-networks/qca9880
AR9580-AR1A | Atheros (now Qualcomm Atheros) | WLAN SoC | -
ATMLH352 | Atmel (now Microchip) | Display controller | https://commons.wikimedia.org/wiki/File:Gigaset_DA810A_-_LCD_display_-_controller_-_Atmel_H3522EC-9644.jpg
APL5932A | Anpec | Linear Regulator | https://pdf1.alldatasheet.com/datasheet-pdf/view/1070998/ANPEC/APL5932A.html
(...) | (...) | (...) | (..)

## Slide 68: Day 3

## Slide 69: External Interfaces
UART

## Slide 70: UART
Universal Asynchronous Receiver/Transmitter
Some context:
  UART is NOT a “hardware protocol”– this is a common misnomer
  A UART is a chip (or a circuit within a chip) used for serial communication
  Various serial protocols can be transmitted via UART:
    RS232
    RS485
    TTL (raw transistor voltage levels)
  We will focus on TTL serial over UART as this is commonly used in embedded systems for short-link debugging interfaces

## Slide 71: UART
Asynchronous communication means the communicating interfaces are not synchronized by a common clock; rather, Stop/Start signals are used to frame transmitted data
Most UART’s we will deal with are full duplex
  This means they can talk/listen simultaneously
  Some will have input disabled; output is still useful for information gathering

## Slide 72: UART
For 2 UART’s to communicate, they must agree on the following:
  Baud Rate
  Parity bit
  Data size
  Stop bits size
  Flow control
Common configuration: 8 data bits; no parity bit; 1 stop bit (“8-N-1”)
Most common Baud Rates: 9600, 57600, 115200 bps

## Slide 73: UART
Note from the first block diagram that the UART receives a clock signal from an external system
As a mere receiver/transmitter, it also receives data (and logic-levels) from the controlling system
To communicate with this interface, we need our own UART; we’ll connect:
  our receiver to their transmitter
  our transmitter to their receiver

## Slide 74: UART
To interface via UART using a test computer, will need a TTL Serial – USB adaptor
  FTDI IC’s are typically used, though generics/copies exist
  Most off-the-shelf serial tools are just an FTDI chip, or generic equivalent, on a breakout board (e.g. the Mini-Module)

## Slide 75: UART
On our target PCB we likely won’t see the UART itself, we’ll see its pins ‘broken out’ in the form of pads, pins, through-holes, etc.
  The interface/pins may or may not be labeled in silkscreen
  Pins may be grouped or separate
  Interface may be grouped w/others
If UART is exposed as 2 random test points, it may be
TRICKY to find!

## Slide 76: UART
The interface typically includes 2-4 pins:
  Tx – most important pin; this transmits the signal we’re interested in
  Rx – combined w/Tx we have an interactive console (if present/enabled)
  GND – we don’t need this; the PCB shares one common ground, so we can replace this with any grounded surface on the board including pins, shields, screws, etc.
  Vcc – Reference voltage; we will NOT use this pin if present

## Slide 77: UART - Exercise
Let us assume the interface shown is a UART
Using what we’ve learned about copper pads:
  Can you immediately spot the GND pin?
  How about the Vcc (power) pin?
  Can verify by probing!
With 2 pins identified, that leaves Rx/Tx – we can determine which is which by trial and error using our receiver
  Rx to Rx: nothing will happen
  Rx to Tx: we should see data
  Alternatively: find by probing!

## Slide 78: UART
With pinout identified, we’re ready to attempt a connection
Serial adapters, when plugged in, should be visible from the test system:
  Linux – ‘/dev/ttyUSB0’ for instance
  Windows– serial COM port
Access using any serial communication program
  i.e. screen, minicom, etc.
  Using screen: “screen /path/to/adapter [baud rate]”
  Example:

## Slide 79: UART – Determining Baud Rate
Method 1: Measuring
Probe transmitter pin using oscilloscope or logic analyzer WHILE device is running
Record wavelength of captured signal
Baud Rate ≈ ⅟(wavelength / 2)
Example shown:
  wavelength/2 ≈ 17.36us
  1/wavelength ≈ 57600bps

## Slide 80: UART – Determining Baud Rate
Method 2: Trial-and-Error
Try common baud rates and observe the output
  Correct rate will yield readable ASCII output
  Clock mismatch will result in mutilated output (pictured)
Many open-source tools exist to automate this for saving time
  https://github.com/biw/Baudrate.py
  https://github.com/sickcodes/python3-baudrate
  https://github.com/devttys0/baudrate/blob/master/baudrate.py
Easy project– try writing your own script for Baud Rate Detection!

## Slide 81: UART
If successful, we can interface directly with our embedded device
What we may find:
  Console/shell access
  Boot menu
  Peripheral controls (e.g. SPI)
  Filesystem
  Verbose Chip/Storage specs
  Plenty more…
In addition to the UART itself, what we find may assist with other attack vectors!

## Slide 82: Case Study: UART

## Slide 83
Using the methods discussed in this lesson, connect to the target device using the POPULATED header indicating UART (as shown)

## Slide 84
Recall the lesson on baud rate detection…
If done correctly, the console should display the boot sequence

## Slide 85
The console will spit out information very quickly
To capture for review, we can use the ‘screen’ commands logging feature
Now we can go back and mine our .txt file for useful tidbits
  e.g. We can see right away this is the Cortina chip (main controller)
  Note the JTAG ID for later!

## Slide 86
If we hit enter when the device is operational, we can get a shell!
Unfortunately, it’s password protected…
Assuming we don’t know the password, there’s MUCH more we can do 
Note: this password hash is compiled via the CONFIG_AUTOBOOT_STOP_STR_SHA256</config> setting
  Can we use an environment variable to override this??
  (see U-Boot shell next)

## Slide 87
Notice they left us access to the U-Boot shell
  This is often mitigated using a boot delay
  If so, this can be bypassed
U-boot is the hacker’s best friend
VERY dangerous for us to have this access

## Slide 88
Take some time to explore all the different help menus, commands, etc.
Some are critical from attack perspective

## Slide 89
Pay close attention to bootcmd and bootargs!
Can you follow the chain of variable names to understand what’s actually executing?
Note all the storage info, addresses, things that might help later…

## Slide 90
Get creative – look for fail-opens, fuses, registers, connected peripherals/storage
  Flash, EMMC, etc.
  SPI, I2C, etc.
  try holding the HW reset button and observe in the console
    Some chip defenses account for SW-based reboots but not HW!
  Can we dump flash for offline analysis?

## Slide 91: External Interfaces
JTAG

## Slide 92: JTAG
Joint Test Action Group
Some context:
  Industry standard for verifying/testing manufactured PCB’s
  Initially for boundary-scan testing (physical interconnects, faults) at board-level
    80’s brought wider use of BGA’s, preventing access to signals
    Limitations of bed-of-nails, flying probes, etc. became evident
    Test fixtures increasingly complex/expensive
    JTAG  test functionality built into IC
  Implementation/uses continually evolve
  Today JTAG may be used for:
    Boundary-scanning
    In-Circuit Testing
    Processor debugging/emulation
    Programming FPGAs/CPLDs
    Storing firmware

## Slide 93: JTAG
Joint Test Action Group
More context:
  Most embedded systems have dedicated debug port for serial communication
  Consumer devices
    Most won’t explicitly provide JTAG connector…
    May be leftover on board from prototyping/production
    If present, may assist in RE or exploit development
  We’ll focus on JTAG as means of MCU firmware extraction

## Slide 94: JTAG
Every JTAG-enabled chip provides at least one TAP (Test Access Port)
Interface design allows multiple chips/TAPs daisy-chained together (like SPI)
Multiple chips can share single debug port on device
Chain of TAPs is called a scan chain

## Slide 95: JTAG
Like SPI, implementations vary; logic signals are usually:
  TDI – Test Data In
  TDO – Test Data Out
  TCK – Test Clock
  TMS – Test Mode Select
  TRST – Test Reset (Optional)
These signals control a finite state machine (within the TAP Controller) as seen on the next slide

## Slide 96: JTAG
TMS is sampled on rising edge of TCK
Mode selects 1 of 2 “paths” (Instruction/Data Register)
Shift registers move data in/out using TDI/TDO

## Slide 97: JTAG
JTAG requires at least 2 Data Registers (more are standardized):
  Boundary Scan register– primary “data” register
  BYPASS register – single-bit pass-through; connects TDI/TDO
JTAG requires at least 4 instructions to be implemented (vendors can add more, standardized or device-specific):
  EXTEST – external boundary scan
  SAMPLE/PRELOAD – boundary scan (during device operation)
  BYPASS – “skip” boundary scan chain (we’ll use to test physical connection)
Most designs also implement the IDCODE instruction
  IDCODE – output device identification stored in IDCODE register

## Slide 98: JTAG
As stated JTAG is vendor/device-specific like SPI
Interface may be “wrapped” in middleware architecture
  Abstracts TAP as well as connected interfaces (flash, ROM, CPU, etc.)
  E.g. ARM chips use ARM’s CoreSight debug architecture
    ARM Debug Interface (ADI): https://piolabs.com/blog/engineering/diving-into-arm-debug-access-port.html
    “DAP” (Debug Access Port) used instead of TAP
    Further granularity for different cores/architectures
    Implemented for both JTAG and SWD (Serial Wire Debug, discussed later)
    For ARM, we can import special library into OpenOCD (discussed later)

## Slide 99: JTAG
Much like UART we’ll see its pins ‘broken out’ in the form of pads, pins, through-holes, etc.
  The interface/pins may or may not be labeled in silkscreen
  Pins may be grouped or separate
  Interface may be grouped w/others
  IF present, the interface may be disabled via hardware or firmware!
    If disabled via hardware we may be able to replace missing pull-up/down resister, fix a severed trace, etc. to re-enable

## Slide 100: JTAG
What if our JTAG port has unlabeled pins?

## Slide 101: JTAG
If we know which pins may contain JTAG, we can discover the pinout by ‘brute force’:
  Try every pin combination
  Each attempt sends IDCODE instruction
  Correct pinout will yield a valid IDCODE
Tools widely used to automate discovery:
  JTAGulator (dedicated HW) – http://www.grandideastudio.com/jtagulator/
  Raspi (open-source scripts) – https://github.com/cyphunk/JTAGenum
  Note: always probe for GND, logic-level first!

## Slide 102: JTAG
What if we don’t HAVE a port…but the interface IS somewhere?

## Slide 103: JTAG
Finding the interface itself can be tricky (sometimes on purpose )
We may have to deduce its location by:
  Chip proximity
  Traces
  Datasheet (if chip known)
  Pin count/grouping (can we spot 5+ pins that look related?)
  Probing!!!
    Do we know the target’s logic level (recall earlier lesson)?
    WILL NEED THIS anyway before interfacing safely
    E.g. SSD controller’s typically use 1.8V for JTAG…see next slide

## Slide 104: JTAG
The previous image showed an opened SSD (solid-state hard drive)
To locate the controller’s JTAG interface, UL:
  Noted a line of 7-8 pins near the target controller
  Checked for voltages ≤ 1.8v, located GND
  Brute-force remaining pins

## Slide 105: JTAG
An example with grouped, plated through-holes:

## Slide 106: JTAG
Manufacturers often use proprietary connectors/fixtures to prevent easy access
How do we locate JTAG in this fine-pitched array of 38 ‘candidate’ pads?

## Slide 107: JTAG
By creating our own bed-of-nails test fixture … remember, creativity is the limit!

## Slide 108: JTAG
Pads are broken-out to standard header size (.1”) for easy jumper-access
Brute-forcing 24 pins at once, we can locate JTAG in 2 quick scans 
Advanced hardware hacking often requires making your own tools/connectors…

## Slide 109: JTAG
Now that we know the pins, we’ll connect using an on-chip debugger
Standard tool is OpenOCD (https://openocd.org/)
  Supports most common chips/cores/etc. (up-to-date)
  JTAG & SWD
  Import libraries for proprietary middleware (i.e. ARM’s CoreSight)
  Local/remote debugging via Telnet+GDB
Countless supported dongles
  Dedicated JTAG Adapters (e.g. Segger J-Link)
    Expensive, with hit-or-miss results
    Adaptors only compatible with certain chipsets
  FT2232 (or equivalent)-based Adapters
    Mini-Module, Bus Pirate, Shikra, etc.
    Recall FTDI chips from UART lesson?
    Used for UART, SPI, JTAG, SWD, I2C, and more…
    Hardware hacker’s “Swiss army knife”!
    Serial IC’s are VERY cheap & dispensible

## Slide 110: JTAG - OpenOCD
Running on Linux: “openocd –f [int.cfg] –f [target.cfg]”
  Interface (adapter) configuration file
    Preinstalled .cfg files for all compatible boards
    Some tools provide their own (e.g. Xipiter’s Shikra)
  Target configuration file
    Preinstalled .cfg files for many common chipsets
    May be available on manufacturer’s site
    No config file?
      If we know the chip, we can build it ourselves from the chip’s datasheet
      If not, we can try “autoprobing”

## Slide 111: JTAG - OpenOCD
Autoprobing
  With no target configured, OpenOCD can automatically check the scan chain for enabled TAPs (note: modern processors may have TAP for each core!)
  For all TAPs identified, output will provide further configuration code
  May STILL need more information to configure out debugger…
  If we can identify CPU cores, developer pages can help us map the chip’s memory
    https://developer.arm.com/documentation/dui0552/a/the-cortex-m3-processor/memory-model

## Slide 112: JTAG - OpenOCD
Looking at the connected ROM table tells us this TAP uses the CoreSight architecture mentioned previously
  As we’ve learned, OpenOCD provides a config file containing the libraries needed for ARM’s interface
  Using ‘DAP’ commands, we must halt the CPU – then we can debug, dump firmware, etc. 

## Slide 113: JTAG – Level-Shifting
Note: When interfacing via JTAG, ALWAYS mind your levels!
  Before you connect anything, determine your target’s required logic-level via probing/datasheet
  Common levels: 1.8V, 3.3V, 5V – depends on target device
Most adapters are 3.3v; if the target is 1.8v, you’ll FRY the target chip
Some tools (e.g. JTAGulator) use built-in level shifters
With most adapters you’ll need your own level shifter
  Choosing the best shifter for any project:
  (Great Resource!)

## Slide 114: JTAG – Level-Shifting
Keep the “magic smoke” inside the chip! (https://en.wikipedia.org/wiki/Magic_smoke)
Always have a backup device – hardware hacking means bricking things

## Slide 115: Case Study: JTAG

## Slide 116
Note the unlabeled 10-pin connector near the Zigbee controller
  As we’ll learn later, the OTHER 10-pin connector has labels indicating an SPI bus
  Tracings/proximity hint this is related to the nearby SoC; perhaps it's for the main controller (broken out for ease-of-use)
Given the number of pins, there’s a chance this connector hosts a JTAG debug port
Connect a JTAGulator (or equivalent) to these pins to find out
A cheap debug cable (shown) can help break out the pins
  Much easier and more robust than small clips, etc.

## Slide 118
Note that we are using 3.3v logic levels
As we learned, this should be checked first with probing
If connected properly, you should see the output shown using a JTAGulator
Pins #’s will differ based on how you are connected
Note: being an ARM CPU (as we’ll see shortly), it’s likely this connector also contains a Serial Wire Debug port which we’ll study briefly later
TDO TDI TCK
GND TMS TRST#

## Slide 119
With pins known, connect using an OpenOCD-compatible adapter
  Ex. Bus pirate (shown)

## Slide 120
Try using the Autoprobing feature mentioned earlier
  https://openocd.org/doc/html/TAP-Declaration.html
  You’ll need the config file for your specific adapter
If connected properly, we should see the same IDCODE’s we found when we determined the pinout
Note the vendor info and # of TAPS

## Slide 121
We COULD use the output we received to write our own config files
However, if you check the available target list you may notice something awfully convenient (good thing we recorded everything earlier)
Let’s try running this readymade config file for ‘em357’ and see if it works…

## Slide 122
It worked, and we’ve identified the ARM processor in use!
Check the ARM developer site for memory map, etc. 

## Slide 123
Explore the ARM debug interface we studied earlier; we now have full access to this CPU
If we halt the chip, we can step instructions, read/write to memory, or create whole firmware dumps
  Check core info for where code is stored
  If unsure…dump, test in disassembler, and dump again (trial-and-error) to obtain full images

## Slide 124
Strings immediately verify we’ve dumped from the EM357
  It appears this debug port is for Zigbee!
  Also note: we DO NOT see the IDCODE for the Cortina chip we noted from the boot log (we know main chip is not on this scan chain)

## Slide 125
Note: make sure you import using correct processor/language type if you’ll be reverse-engineering your dump!

## Slide 126: Day 4

## Slide 127: External Interfaces
SPI

## Slide 128: SPI
Serial Peripheral Interface
Some context:
  ‘De facto’ standard for short-distance wired communication between chips in embedded devices (again – NOT a “hardware protocol”!)
  SPI is a synchronous serial interface– and unlike UART, SPI does not refer to a chip; the term may refer to:
    Chip’s physical interface
    Bus
    Specification
  Used by controllers to interface w/peripherals, such as:
    Sensors
    Displays
    Memory
Attackers primarily interested in accessing flash/EEPROM via SPI

## Slide 129: SPI
Master-Slave architecture
  Master controls communication, provides clocking
  Chip Select allows for “daisy chaining” multiple peripherals
Communication is usually full duplex with four logic signals:
  SCLK – serial clock
  MOSI – master out, slave in
  MISO – master in, slave out
  CS/SS – chip/slave select (depending on configuration)
Naming conventions vary! More examples:
  Master/Slave = Main/Sub
  SCLK = SCK = SCL = CLK
  CE = Chip Enable

## Slide 130: SPI – Chaining Configurations

## Slide 131: SPI
As stated, the SPI bus is a ‘de facto’ standard – NOT a protocol
  Every device defines its own “protocol”
  Duplexity, commands (if supported), signals, word size, active H/L, etc. all vary
  Hardware & connectors also device-specific
Using a specific SPI will require obtaining datasheet using methods discussed earlier

## Slide 132: SPI – Chip-On vs. Chip-Off
Chip-On
As with UART, we may find SPI in some form of breakout or connector on the board
Pins may be labeled; if not, we can determine pinout by:
  Tracing pins to chip legs (remember our multimeter skills?)
  Looking at chip’s datasheet for pin descriptions
Without a port/header we’ll need to connect directly to the chip…

## Slide 133: SPI – Chip-On vs. Chip-Off
Chip-On
Test Clamp (“Chip-clip”)
  Not available for all packages (recall TSOP48 from previous lesson?)
  Not always a secure connection
Test Clips
  Fasten to individual pins
  Small-pitch clips get very pricey 
  Contacts bend/break easily
Micro-soldering to pins
Creativity is the limit…

## Slide 134: SPI – Chip-On vs. Chip-Off
Chip-On
Chip-On interaction prevents us from having to remove the chip, rendering device inoperative
Removed chip may take extreme care/effort to reattach
Why remove a chip for interaction?
  No clamp/clips available
  Difficult pitch
  Chip has no legs (remember some of package types we saw: BGA, QFN, etc.)

## Slide 135: SPI – Chip-On vs. Chip-Off
Chip-Off
Chip usually placed in socket
  Must match chip’s package
  Best to keep sockets for common flash types
Socket connects to chip-reader (”programmer”/”flasher”)
Commercial (“Universal”) Programmer
  Pro’s
    Built-in socket or connector
    Comes with GUI software
    Easy, no knowledge required
    SPI details automated/abstracted
  Con’s
    Expensive
    May ignore proprietary commands
    Only recognizes supported chips – if our chip isn’t supported, we’re on our own!

## Slide 136: SPI – Chip-On vs. Chip-Off
Chip-Off
Open-source CLI tools, i.e. “flashrom”
  Pro’s
    Use our own hardware
    Simple terminal commands
    No knowledge required (aside from chip name)
    SPI details automated/abstracted
  Con’s
    Only recognizes supported chips – if our chip isn’t supported, we’re on our own!
Write our own software
  Pro’s
    Use our own hardware
    Improve our understanding
    Not limited by “supported chips” or compatibility
  Con’s
    Must have datasheet available
    Requires some low-level coding

## Slide 137: SPI – Chip-On vs. Chip-Off
(Quick Note: we can use our own software for Chip-On extraction as well…)

## Slide 138: SPI – Chip-On vs. Chip-Off
Chip-Off
One more Chip-Off method worth mentioning is called “dead-bugging”
  This entails soldering to the pins of a removed chip
  Name after the obvious resemblance shown
  Easy with certain package types (brave hackers have done this to complex BGA’s!)
  Means of physical connection; can be used with paid, open-source, or custom software

## Slide 139: SPI – Chip-On vs. Chip-Off
Chip-Off
Again, creativity is the limit… and sometimes patience

## Slide 140: Case Study: SPI

## Slide 141
Recall the debug port near the Zigbee controller
It appears the SPI connector on the board is for the Z-wave controller
To obtain main device FW via SPI we’ll need to remove the flash chip found earlier
Before building a chip reader, let’s go through a quick example
Similar model from Securifi  Almond 3
  https://www.securifi.com/rg/almond3
  Flash datasheet: https://www.digikey.co.th/htmldatasheets/production/1952774/0/0/1/n25q512a.html
We’ll see how datasheet instructs us to:
  Connect pins
  R/W via bit-banging
  Example command: Read ID
    Outputs manufacturer info

## Slide 142
Find the pin diagram on that datasheet
This tells us how to connect with a microcontroller

## Slide 143
Find the timing diagram for the READ ID command
The code for implementing this command from an Arduino/Redboard is shown on the right
  Note how latching and I/O is done by simply driving digital pins HIGH/LOW
  Datasheet also has specific diagrams for command latching, address latching, and data
  All delays/times are documented as well

## Slide 144
When run from a terminal using ‘screen’, we receive the output expected based on the datasheet
Reading ID is a perfect ‘test command’ to ensure the chip-reader is working
  Typically the easiest/quickest to write and test
  If working, THEN move to reading firmware (which may take some time)
Now, try developing the same type of chip reader for the Almond+ using the datasheet we found earlier from Spansion

## Slide 145
First step is to carefully remove the chip using a heat gun and place in a TSOP48 (– DIP48) socket
(If possible, soaking removed chip in isopropyl alcohol briefly will clean oxide layer to prevent shorts in socket)

## Slide 146
Referring to the Spansion datasheet, determine which pins are needed and how we’ll need to use them
Recall what we learned about SPI and how details vary b/w vendor implementations
  Pins are slightly different than the Micron chip
  More signals needed

## Slide 147
When ready to connect, make sure you understand how the chip socket breaks out the IC pins...

## Slide 148
This is what proper connection looks like using a microcontroller
  May look neater than this…
  Use breadboard if big enough
  M-F jumpers very helpful

## Slide 149
Once connected, find the Read ID command
Study timing/latching diagrams, I/O bytes, etc.
As in the example before, try converting this command to bit-banging code
  Begin w/pseudo code
  Decompose systematically into easy algorithms
    Ex. sending command:
      Enable chip/CL
      WE low
      [output command]
      WE high
      Disable CL

## Slide 150
Run using ‘screen’ in terminal to test your code
If done correctly, will output the bytes indicated in the datasheet (shown right)
After Read ID try implementing other commands
  E.g. ‘Page Read’ command (try iterating through all pages)
  Often more than 1 way to pull the entire firmware; try finding the most ‘elegant’ (or fastest) way…
If unsuccessful  don’t worry! We will obtain firmware through other means!

## Slide 151: External Interfaces
Other Common Standards

## Slide 152: ISP/ICSP
In-System Programming / In-Circuit Serial Programming
Programming/updates after IC installation
Most MCU manufacturers implement their own variant
  Ex. Atmel, AVR, Microchip
  Integrate coding/testing (save $$$/time)
  Serial int. requires less real estate on PCB than specialized connector
  No need to buy pre-programmed from distributor
Vendor provides specialized programmer/debugger
Ex. Microchip’s PIC
  MPLAB ICD
  PICkit

## Slide 153: ISP/ICSP
PIC on this IoT router – what does it do??
  Dump in MPLAB IDE
  RE time…
    Flavor = Intel
    Language = PIC16F

## Slide 154: ISP/ICSP
PIC on this IoT router – what does it do??
  ‘Reset’ function
  Interrupt handling routines
    Read Peripheral Interface reg.
    Read Synchronous Serial Port reg.
Should have made use of PIC’s configuration fuses to prevent readout!

## Slide 155: I2C
Inter-Integrated Circuit
Short-distance serial communication bus; connects controller to low-speed peripherals
  Used for low cost & simplicity
  Less overhead than UART
  Fewer pins than SPI
Design
  Clock (SCL) and Data (SDA) lines
  Bi-directional, Master/slave architecture (chainable)
  Protocol/messages on bus are device-specific

## Slide 156: SWD
Serial Wire Debug
Essentially a modified version of JTAG for ARM processors
Same protocols using only 2 pins
  SWDIO (data)
  SWCLK (clock)
  May share JTAG pins (dual-mode programmers)
    TMS  SWDIO
    TCK  SWCLK

## Slide 157: Day 5

## Slide 158: Case Study: Firmware Update

## Slide 159
If FW was not obtained from the device itself, we can grab an update from the Securifi support page (https://www.securifi.com/rg/support)
  Follow link under Software
  Select ALMOND+ for Step 2
  Select ‘Download’ under Step 4

## Slide 160
A quick peek at this download reveals the following:
  U-boot wrapped image
    uImage header
    zImage (compressed Linux kernel)
  Archive (gzip)
  Squashfs filesystem (lzma)

## Slide 161
Digging further:
  U-boot wrapped image
    uImage header
    zImage (compressed Linux kernel)
  Archive (gzip)
    Archive (cpio) – special char files
    Archive (lzo) – linux config file
  Squashfs filesystem (lzma)
  Try carving different ‘pieces’ with ‘dd’ tool
  Other things: strings, checksums, DER certs, etc.

## Slide 162
We’re most interested in the filesystem
As this is a downloaded update, we won’t find user data/secrets (can still find default passwords, etc.)
We CAN find product-wide vulnerabilities/bugs
Investigate:
  System binaries
  Shell scripts
  Config files
  Lots of proprietary code!
  Any info assisting further attacks
  Network interfaces especially interesting
    Check SW behind ‘newer’ libraries/protocols
    i.e. Zigbee/Z-wave

## Slide 163: Case Study: Threat Modeling

## Slide 165
Recall typical architecture studied earlier
Let’s revisit our board now that we understand the chips & interfaces…

## Slide 166
Debug – Zigbee controller
UART – Zigbee controller(?)
HW Reset
SPI – Z-Wave controller
UART – Z-Wave controller(?)
HW Reset
Serial USB
UART – Main IC
SPI – NAND flash
(back side)

## Slide 167
Main Controller
SDRAM
Flash
Z-Wave Controller
Zigbee Controller
LCD
WLAN Controller 1
WLAN Controller 2
Ethernet Switch
What sort of damage can be done considering our large attack surface?
Consider all device functions explored…
Don’t forget connected devices/networks
  Ethernet/Wi-Fi
  Connected IoT devices
  How can we impact these from our vulnerable device?
  How can we attack the device from each network?
  What sort of data enters/leaves each route?
USB

## Slide 168
In addition to the main chip, we’ve determined we can obtain FW (and possibly console/boot/debugging access) for 2 other controllers (which are likely ‘sensitive’)!
Review the various threats/impacts around each device
  Fuses, drivers, libraries, encryption, privileges, etc.
Combine understanding of all HW & SW investigated; build a “treasure map” of attack routes
Consider access (local, remote; privileged, unprivileged; etc.)
To complete our case study, try putting together a threat model for the Securifi Almond+

## Slide 169
Remember key areas to focus on in a time-bound assessment
Although we’ve focused on the hardware, keep in mind there is MORE to this attack surface
  Web application
  Mobile application (Android/iOS)
  Wireless communication
Ideal penetration test will encompass these as they are inherently connected
We’ll NEED compatible smart devices for thorough testing…

## Slide 171: Conclusion

## Slide 172
Concepts covered:
  State of HW Security
  Device Teardown
    PCB Analysis
    Component/Datasheet Lookup
  Integrated Circuits
  External Interfaces
  Boot Security (U-boot)
  On-Chip Debugging
  Datasheet Analysis
  Firmware Extraction/Analysis
  Threat Modeling

## Slide 173
Further learning/practice:
  Write a script for baud rate detection
  Build a more advanced chip reader
    Sends multiple commands
    CLI arguments
    Practice different vendors/packages
  Try the UNPOPULATED UARTS we didn’t explore
    Extract FW
    Find bugs in SoC’s
  Can you attack serial USB?
  Investigate all SoC's
  Reverse-engineer Securifi binaries
  Search known vulnerabilities
    Lots of OLD chips/libraries
    Old version of U-boot (MUST be a gold mine)
  Find device w/other buses and protocols to investigate
    e.g., I2C, SWD, CAN
  Assess any new device you can get your hands on… hardware skills come with LOTS OF PRACTICE!!!